## Slide 1: PerkLab research methodology overview
Andras Lasso, PhD
Associate Director
Laboratory for Percutaneous Surgery (PerkLab)
School of Computing
Queen’s University, Kingston, ON, Canada

## Slide 2: PerkLab
About 20-25 members
From computer science, electrical engineering, and mechanical engineering departments and medical school
1/4 undergrad 1/4 Masters 1/4 PhD, postdoc 1/4 faculty, staff research engineers – continuity
Research focus:
Percutaneous interventions
Image guidance
Tool navigation
Translational research

## Slide 3: Scope
From algorithms to tools
Can it be done?
  Prototypes
Is it worth doing?
  Tools for translational research
Standard of care
  Commercially available clinical “devices” with regulatory approval
Ron Kikinis, Harvard SPL, 2012

## Slide 4: Reproducible research – theory
Scientific method: propose hypothesis, prove it by experiments
Mistakes, bias, … => repeatability
Full specification Victoria Stodden, Enabling reproducible research: licensing for scientific innovation
  Research paper
  Data (with description the data, how it was acquired, processed, including the source code that was used for processing, …)
  Experiment (source code, instructions, parameters, …)
  Results (source code, documentation, data, …)
Reduced duplicate efforts, higher credibility, higher quality outcome, community, …
J.P.A. Ioannidis, Why Most Published Research Findings are False, PLoS Med 2(8), 2004

## Slide 5: Reproducible research – practice
By default openly available source code, full documentation, all data
Permissive license – no strings attached
  BSD: redistribution, modification, … all allowed
    Provided as is
    Don’t use the author name for endorsement
    Don’t remove the license
Can we afford to give away all these?
  Full disclosure mostly delayed until publication
  Exceptional ideas are patented before publication
  Maintain competitive advantage by continuous improvement
  We get a lot in return

## Slide 6: Industry best practices
Brought in by industry-trained staff members
Adopt procedures that increase quality & productivity
Keep overhead at the minimum
  Usually no need to comply to external regulations (Health Canada, FDA, CE, …), just institutional ethics board
Learning these: investment with a short payback period

## Slide 7: Planning, design, implementation
Web-based, integrated project management: GitHub or GitLab
  GitHub: everybody is there, unlimited public repositories for free; free private repositories for university research labs; free continuous integration
Provided services:
  revision control
  code review
  issue tracking: issues, releases, milestones, project boards
  continuous integration: automated testing, documentation generation
  website hosting, wiki
  discussions (very limited), no private messaging

## Slide 8: Planning, design, implementation
Documentation:
  User manual:
    Tutorials (PowerPoint, YouTube)
    Reference manual (description of the software)
  Developer manual:
    Tutorials
    Examples, tests
    API documentation (Sphinx for Python, Doxygen for C++)
    Design documentation
  Hosting: readthedocs, github pages

## Slide 9: Verification
Automatic build and test (many frameworks for Python; CMake/CTest for C++)
Automated GUI testing is hard
Continuous integration: GitHub actions, CDash
CTest results reported on CDash

## Slide 10: Validation
Fidelity levels: Simulated < Synthetic phantoms < Animal tissue (butcher shop) < Cadaver < Patient
Ethics approval: required for human subject studies (even if just filling out a form), evaluation on patient cases
Phantoms:
Hard tissue (bone): 3D printed, with Barium coating for X-ray visibility
Soft tissue: water based (agar, gelatin), PVC, silicon
Skin: super soft silicon rubber
Vessels: rubber tubes
Targets, validation points
http://perk-software.cs.queensu.ca/plus/doc/nightly/modelcatalog/

## Slide 11: Software platform

## Slide 12: Medical image computing software ecosystem (desktop+server)
pydicom
DCMTK
3D Slicer
OpenIGTLink
Data analysis algorithms
SciPy
User interface
Visualization
Applications
Communication
Libraries, toolkits, packages

## Slide 13: 3D Slicer architecture
hardware
OpenIGTLink
Registration
Segmentation
...
3D Slicer
Calibration, synchronization, pre-processing, simulation, record&replay
Visualization
SlicerIGT
Pivot calibration
PLUS
software
SlicerJupyter
Python, VTK, ITK, CTK, Qt, DCMTK, …
...
ProstateNav
Device interface
LumpNav
...
Slicelets
(custom Slicer applets)
...
Tool watchdog
Model registration
Breach warning
Slicer extensions
DICOM
OpenIGTLink
Quantification
hundreds of devices (imaging, position tracking, various sensors, and manipulators)
Ultrasound
scanners
Robotic devices, manipulators
Navigation
systems
Surgical microscopes, endoscopes
MRI, CT, PET scanners
0.01%
DICOMweb REST API
SlicerWeb
Slicer VirtualReality
Notes: Using OpenIGTLink (which is a Network Interface for Image-Guided Therapy), PLUS can stream this data in real-time to 3D Slicer and can also be used for pre-processing, and calibration for navigated image-guided interventions.

## Slide 14: Summary
Translational research
Reproducible research
Industry best practices
Building on one platform