## Slide 1
3D Slicer DICOM Tutorial

## Slide 2: Prerequisites
Please finish the ‘Data loading and visualization’ tutorial before starting this one
Install the DICOMwebBrowser and SlicerRT extensions from the Extensions Manager
Download and unzip this dataset: https://github.com/PerkLab/PerkLabBootcamp/raw/master/Data/eclipse-8.1.20-phantom-prostate.zip

## Slide 3: Digital Imaging and Communications in Medicine (DICOM)
The industry standard for storage and network transfer of medical images
Freely available
  Full documentation: http://medical.nema.org
  DICOM tag lookup: http://dicomlookup.com
“Designed by committee” - many device manufacturers collaborate to specify the standard
Very large (about 3500 pages), complex → implementation is difficult
There is no reference implementation or standard conformance test suite
Implementation is always only partial and very often incorrect

## Slide 4: Digital Imaging and Communications in Medicine (DICOM)
DICOM file structure
  Meta-information header (version, encoding, endianness, etc.)
  List of attributes
    Attribute name: human-readable name
    Tag: 4+4 digit hexadecimal identifier (group+element)
      Even group number: standard data
      Odd group number: private data (see DICOM conformance statement)
    Type: 1 = mandatory, 2=may be empty, 3=may be missing; 1C, 2C, 3C: conditional, it depends on other attributes if required or not
    Description: specification of the attribute
    Value representation (VR): decimal string, date, time, code string, etc. Special: sequence (SQ) can contain a list of attributes
    Value multiplicity (VM): 1, 2, 1-n (string separator: backslash)
  Pixel data is stored in an attribute, too

## Slide 5: Digital Imaging and Communications in Medicine (DICOM)
Most important parts of the standard
  Part 3: Information Object Definitions (IOD): an IOD represents the acquired image (CT, MR, US, etc.); this part specifies the required attributes for each IOD
  Part 5: Data Structures and Encoding: definition of how the data is stored in memory, explains private, conditional, sequence, etc.
  Part 6: Data Dictionary: tag, name, VR, VM for each attribute

## Slide 6: Digital Imaging and Communications in Medicine (DICOM)
Part 3:

## Slide 7: Digital Imaging and Communications in Medicine (DICOM)
Part 6:
Part 5:

## Slide 8: Digital Imaging and Communications in Medicine (DICOM)
DICOM conformance statement
  Publicly available for all DICOM compliant devices
  Describes what parts of the standard are implemented and specifies all the private fields.

## Slide 9: Digital Imaging and Communications in Medicine (DICOM)
Header and attributes are not human-readable

## Slide 10: Digital Imaging and Communications in Medicine (DICOM)
Use the free, open-source dcmdump tool to print it in a human-readable form (part of the DCMTK toolkit)
(0008,0008) CS [ORIGINAL\PRIMARY\AXIAL] # 22, 3 ImageType
(0008,0012) DA [20110922] # 8, 1 InstanceCreationDate
(0008,0013) TM [161402] # 6, 1 InstanceCreationTime
(0008,0016) UI =CTImageStorage # 26, 1 SOPClassUID
(0008,0018) UI [1.2.840.113619.2.55.3.671756986.106.1316467036.466.1] # 52, 1 SOPInstanceUID
(0008,0020) DA [20110920] # 8, 1 StudyDate
(0008,0021) DA [20110920] # 8, 1 SeriesDate
(0008,0060) CS [CT] # 2, 1 Modality
(0008,0070) LO [GE MEDICAL SYSTEMS] # 18, 1 Manufacturer
(0008,0090) PN (no value available) # 0, 0 ReferringPhysicianName
(0008,103e) LO [PELVIS CURATIVE] # 16, 1 SeriesDescription
(0008,1090) LO [LightSpeed RT16] # 16, 1 ManufacturerModelName
(0010,0010) PN [RANDO^PROSTATE] # 14, 1 PatientName
(0010,0020) LO [TEST PHYS PROSTATE] # 18, 1 PatientID
…
(0020,0032) DS [-250\-250\105] # 14, 3 ImagePositionPatient
(0020,0037) DS [1\0.0\0.0\0.0\1\0.0] # 20, 6 ImageOrientationPatient
…
(0028,0010) US 512 # 2, 1 Rows
(0028,0011) US 512 # 2, 1 Columns
(0028,0030) DS [9.76562e-1\9.76562e-1] # 22, 2 PixelSpacing
(0028,0100) US 16 # 2, 1 BitsAllocated
(0028,0101) US 16 # 2, 1 BitsStored
(0028,0102) US 15 # 2, 1 HighBit
(0028,0103) US 0 # 2, 1 PixelRepresentation
(7fe0,0010) OW 0018\0018\0018\0018\0018018\0018\0018... # 524288, 1 PixelData

## Slide 11: Digital Imaging and Communications in Medicine (DICOM)
Use the free, open-source dcmodify tool to add/remove/modify tags for:
Anonymization (removal of information that can identify the patient)
Fixing of invalid files (e.g., too much info was removed when anonymization was done)
Generating synthetic data sets
dcmodify.exe --modify 0028,0030=0.14\0.14 --modify-from-file 7fe0,0010=image0.raw inputslice1.dcm

## Slide 12: Set up DICOM database
Click “DCM” icon and if offered then click “Create new database” button.

## Slide 13: Set up kheops account
Click Demo.
Login with GitHub/Google or register a user.

## Slide 14: Open study from Kheops /1
Click Slicer icon of study INCISIX.

## Slide 15: Open study from Kheops /2
Drag-and-drop the volume to 3D view for volume rendering.

## Slide 16: Create new album
Select CEREBRIX, PELVIX, MAGIX.
Add to an album.
Add to a new album.

## Slide 17: Set album properties
Set Album Name.
Enable all options.
Click Create.

## Slide 18: Create sharing link
Click link icon.
Enable all options.
Click Create.
Save the sharing URL.

## Slide 19: Load using DICOMweb browser
Use sharing link as server URL: https://demo.kheops.online/view/sFy9ca1ncU1otUsJtKva2s
Click Connect.
Select CEREBRIX, series number 6.
Click Download&Load.

## Slide 20: Switch to DICOM module
Notice that the DICOM data is organized in a patient/study/series structure.

## Slide 21: Explore DICOM information
Click Show DICOM database.
Right-click on Series. Click View DICOM metadata.
Double-click the tag to open DICOMLookup.

## Slide 22: Part 2: Using DICOM data from local storage

## Slide 23: Import DICOM data from disk
Open the DICOM module.
Drag-and-drop folder to the Slicer application window.
When DICOM module is opened then drag-and-dropped files are automatically imported as DICOM.

## Slide 24: Load prostate phantom RT data
Double-click on the study to load the entire study.

## Slide 25: Explore radiotherapy dataset
You can show the dose volume in the foreground layer to overlay it with the anatomy:
Link views.
Select 5 as foreground, 2 as background
Use the slider to adjust opacity.

## Slide 26: Part 3: Export DICOM
Slicer DICOM database
DICOM
import
DICOM files
DICOM
export
Remote PACS
DICOM
push
DICOM
query/retrieve
DICOM
loading
Slicer scene

## Slide 27: Export image to DICOM files 1

## Slide 28: Export image to DICOM files 2
Must to set valid sex (e.g., M)

## Slide 29: Export image to DICOM files 2
Right-click on the exported study.
Select Send to DICOM server.
Select DICOMweb protocol.
Use Kheops sharing URL as destination address.
Click OK.

## Slide 30: Export image to DICOM files 2

## Slide 31: Thanks for participating!