## Slide 1
Csaba Pinter
3D Slicer Data Loading and Visualization Tutorial

## Slide 2: Tutorial dataset
Please download the following dataset:
http://slicer.kitware.com/midas3/download/?items=330421,1
Unzip it to a local folder (this step is different for each operating system)

## Slide 3: 3D Slicer version 4.10
The default start-up module is the Welcome module

## Slide 4: Welcome module
Each module of Slicer includes a series of tabs, which gives access to different functionalities.
Click on the arrow symbol to display the content of each tab

## Slide 5: Welcome module
The Documentation & Tutorials section contains useful links to different parts of the Slicer training content.

## Slide 6: Main user interface
Toolbar
Module panel
Data probe
3D view
Slice views

## Slide 7: Load data from computer
Browse to the location of the MR dataset MR-Head.nrrd Drag & drop it into Slicer
Slicer automatically opens the ‘Add data into the scene’ window.
Click OK to load the volume.

## Slide 8: Load data from computer
The axial, sagittal, and coronal views automatically show the loaded volume

## Slide 9: Switch layout
Click on the Slicer layout button

## Slide 10: Switch layout

## Slide 11: Slice view options
Position your mouse cursor over the pin icon to display the slice view toolbar

## Slide 12: Slice view options
Once the slice viewer toolbar is shown, click on the “>>”

## Slide 13: Show ruler

## Slide 14: Rotate to volume plane
Often, MRI volumes are not axis-aligned. To show the true axial view, click the ‘Rotate to volume plane’ button.
Note: This image will not be affected, but many DICOM MR images need to be aligned.

## Slide 15: Foreground image
Images can be overlaid (“fused”) by setting the foreground image.
Note: There is no other image in the scene at this point.

## Slide 16: Switch to conventional layout

## Slide 17: Link views
After linking views, if any setting is changed in a 2D view, all others follow.

## Slide 18: Show slices in 3D
Now the slice views are linked. If you click the ‘Toggle slice visibility in 3D view’ button, then all slices will show up.

## Slide 19: Show slices in 3D
All three anatomical slices are shown in the 3D view

## Slide 20: Navigating the 3D view
Use the left mouse button to rotate, and the right mouse button to zoom in and out

## Slide 21: Close the scene

## Slide 22: Part 2: 3D visualization of surface models of the brain

## Slide 23: Load tutorial scene
Drag and drop the file 3DHeadScene.mrml into Slicer, then click OK

## Slide 24: Center view
Click on the small box icon to center the view, in 3D or in 2D

## Slide 25: Explore loaded data
You can use the module list, or the favorite module toolbar to switch to the Data module

## Slide 26: Explore loaded data
The Data module shows all the data in the scene.
The data items (“nodes”) can be shown/hidden, renamed, deleted, cloned, etc.
Hide the ‘Skin’ model by clicking the eye icon.

## Slide 27: Subject hierarchy
For list of “subject hierarchy” options for a certain node, right-click it in the list. Note that the options are different for each node type.
Right-click the volume called ‘grayscale’.

## Slide 28: Node actions
Choose the Rename option and rename the volume to ‘MR brain’

## Slide 29: Create folder
Scroll down to the bottom, right-click the empty area, then choose ‘Create new folder’.

## Slide 30: Select multiple nodes
Scroll back up, click the topmost model, hold down Shift, and click the last model.
Note: You can use Control/Cmd button to select individually.

## Slide 31: Move nodes to folder
Drag&drop models into the folder

## Slide 32: Hide all nodes in folder
The visibility icon of the folder shows partial visibility because the skin is hidden.
Click that button to hide all nodes in the folder.

## Slide 33: Display options
Right-click the eye icon to see display options

## Slide 34: Volume rendering
Note: the Volume Rendering module is also accessible from the modules list

## Slide 35: Show volume rendering
If your computer has a capable graphics card, change the rendering option to ‘VTK GPU Ray Casting’.
Note: Most computers should be capable.

## Slide 36: Show volume rendering
Click the eye icon to show volume rendering.

## Slide 37: Show volume rendering
For most volumes the default volume properties are not optimal. You need to select a preset.

## Slide 38: Show volume rendering
Select the ‘MR-Default’ preset

## Slide 39: Show volume rendering
Adjust Shift to optimize visualization

## Slide 40: Show models again
Turn off volume rendering using the eye icon.
Switch back to the Data module using the Modules history.

## Slide 41: Show models again
Show the folder again by clicking the closed eye icon in its row.

## Slide 42: Models module
Switch to the Models module form the module list or the favorite modules toolbar.

## Slide 43: Show axial slice in 3D

## Slide 44: Change skin model opacity
Double-click the opacity column for the Skin model, and adjust the slicer to around 0.30

## Slide 45: Hide skull model

## Slide 46: Show coronal slice in 3D

## Slide 47: Model clipping
Select ‘hemispheric_white_matter’, then scroll down to the 3D Display section

## Slide 48: Model clipping
Turn on Clipping

## Slide 49: Model clipping
The optic chiasm becomes visible in the 3D view

## Slide 50: 3D display options
Hide the coronal (green) plane. Position your cursor over the pin icon in the 3D view to display the 3D display options. Select the A (Anterior) view.

## Slide 51: Save the scene
Click the ‘Save data’ button.
Note: Also accessible from the File menu

## Slide 52: Save the scene
The Save Scene and Unsaved Data window lists all elements of the scene.
Double-click the scene (3DHeadScene.mrml), and rename it to myNewScene.mrml. Click Save

## Slide 53: Close the scene

## Slide 54: Load your scene
Load the new scene using the Load Data dialog, or the previously used method of drag and drop.

## Slide 55: Thanks for participating!