## Slide 1
3D Slicer Registration Tutorial

## Slide 2: Prerequisites
Please finish the ‘Data loading and visualization’ tutorial before starting this one: https://www.slicer.org/wiki/Documentation/Nightly/Training#Slicer4_Data_Loading_and_3D_Visualization
Install the SegmentRegistration and SlicerElastix extensions from the Extension Manager

## Slide 3: Part 1: Image-based registration with BRAINS

## Slide 4: Load sample brain tumor images
Click on the ‘Download Sample Data’ button in the Welcome module.

## Slide 5: Load sample brain tumor images
Click ‘MRBrainTumor1’ to download the first dataset. Once it appeared, click ‘MRBrainTumor2’ to download the second one.

## Slide 6: See difference between images
Open the slice view controller by placing the mouse cursor over the pin icon. Click the ‘>>’ button to expand the path selector. Link the views with the link button.
Click the foreground image selector and choose ‘MRBrainTumor1’

## Slide 7: See difference between images
Adjust contrast and brightness (“window width and level”) by holding down the left mouse button on the slice viewer and moving it up/down for window level, and left/right for window width.

## Slide 8: See difference between images
Adjust the opacity slider to see both volumes at the same time.

## Slide 9: See difference between images
Switch to the Volumes module, then change the lookup table for the first volume to ‘Red’.

## Slide 10: See difference between images
Select the second volume, then change its lookup table to ‘Green’.

## Slide 11: Register image using BRAINS
Switch to the ‘General Registration (BRAINS)’ module.

## Slide 12: Register image using BRAINS
Select fixed and moving image volumes, then create an output linear transform. Name it ‘MRBrainTumor2ToMRBrainTumor1Transform’

## Slide 13: Register image using BRAINS
Scroll down in the module. Select the ‘Rigid (6 DOF)’ registration phase, then click Apply.

## Slide 14: Deformable registration using BRAINS
Create new BSpline transform with the name ‘MRBrainTumor2ToMRBrainTumor1BSplineTransform’.

## Slide 15: Deformable registration using BRAINS
Deselect linear transform and Rigid (6 DOF) phase. Select the linear transform as Initialization transform, check ‘BSpline (>27 DOF)’, then click Apply.

## Slide 16: Deformable registration using BRAINS
Note that you can do both phases at the same time.
See how well the two images now match.

## Slide 17: Part 2: Fiducial-based registration

## Slide 18: Restart workflow
Close the scene (see File menu), and load the two sample brain tumor images once more.

## Slide 19: Switch to 3D only layout

## Slide 20: Switch to Volume Rendering

## Slide 21: Show brain MRI in 3D
Click the eye icon to show MRBrainTumor1, then click the preset selector and choose MR-Default on the bottom.

## Slide 22: Show brain MRI in 3D
Make sure VTK GPU Ray Casting is the active rendering mode if your computer has a GPU.
Adjust the Shift slider to optimize display.

## Slide 23: Show brain MRI in 3D
Optionally set the GPU memory size, and switch to Normal quality and enable Surface smoothing if your computer is fast enough.

## Slide 24: Place first set of fiducials
Use the Create-and-Place fiducials button on the toolbar to place fiducials.
Place fiducials in the following order:
Corner of right eye (which is on the left)
Bridge of the nose
Corner of left eye

## Slide 25: Place first set of fiducials
Place two more fiducials
4. Where the top of the right ear meets the head
5. Same for left ear

## Slide 26: Create second set of fiducials
Switch to the Markups module using the toolbar. Create a new fiducial list for the second set.

## Slide 27: Place second set of fiducials
Hide MRBrainTumor1, switch to MRBrainTumor2, show it and set up display, then place the second set of fiducials the same way:
Corner of right eye (which is on the left)
Bridge of the nose
Corner of left eye
Where the top of the right ear meets the head
Same for left ear

## Slide 28: Switch to Fiducial Registration
Note that the Landmark Registration module can do the same task in a different way, as well as the Fiducial Registration Wizard in SlicerIGT.

## Slide 29: Perform fiducial registration
Make the marked selections and click Apply.

## Slide 30: Apply transform on image
Switch back to Four-Up layout and show both volumes. Go to Data module. Double-click the transforms column for MRBrainTumor2, then select the just created transform.

## Slide 31: The two images are now aligned

## Slide 32: Segment Registration
Registration types: None / Rigid / Affine / Deformable

## Slide 33: SlicerElastix

## Slide 34: Thanks for participating!

## Slide 35: Appendix

## Slide 36: Alternative method of comparison
Switch to the Segment Editor module, make sure MRBrainTumor2 is selected as master volume, and add a new segment.

## Slide 37: Alternative method of comparison
Select the ‘Threshold’ effect, adjust the threshold range so that the highlighted region contains structures in all regions and has a mostly clear border, then click Apply.

## Slide 38: Alternative method of comparison
Link slice views, then change segmentation visualization to outline only (or you can keep the default if you prefer that).
Show MRBrainTumor1 in the background layer.