## Slide 1: Coordinate systems and transforms in IGT

## Slide 2: Navigation
Data collection
Registration
Visualization

## Slide 3: The Train Fly Problem
Two trains are on the same track 100 km apart heading towards one another, each at a speed of 20 km/h. A fly starting out at the front of one train, flies towards the other at a speed of 40 km/h. Upon reaching the other train, the fly turns around and continues towards the first train. This is repeated until the two trains crash and the fly is annihilated. How many kilometers does the fly travel before the crash?

## Slide 4: Coordinate system
X
Y
Z
- Where is a point?
- (X,Y,Z)
- Where is (0,0,0)?
- Which direction is X, Y, and Z?
- How much is 1?
Remember: define coordinate systems
Use right-handed
Tell origin
Tell directions
Tell units

## Slide 5: Where is the probe?
X
Y
Z
Tracker
Attach a coordinate system to everything that is not rigidly fixed to an already existing coordinate system.
Name coordinate systems consistently.
Define points WITH respect to coordinate systems.
X
Y
Z
Probe
Relative to what?
Note:
There is no absolute "world" coordinate system!

## Slide 6: Coordinate transform
X
Y
Z
X
Y
Z
Reference
Tracker
Tracker-To-Reference-Transform
Transforms
describe every linear spatial relationship
internally represented by 4x4 matrices
concatenated by matrix multiplication
X
Y
Z
Probe
Probe-To-Reference-Transform
Probe-To-Tracker-Transform
P→R = T→R * P→T

## Slide 7: Transform
X
Y
Z
X
Y
Z
One
Other
OneToOtherTransform
Types of transforms
Rigid
  Translation
  Rotation
Similarity
  Isotropic scaling
Affine
  Anisotropic scaling, skew
Deformable (non-linear)

## Slide 8: Transforms (PLUS)
All transforms are defined by the names of the two coordinate systems that it transforms between:
<FromCoordinateSystem>To<ToCoordinateSystem>Transform = <Rxx> <Rxy> <Rxz> <Tx>
<Ryx> <Ryy> <Ryz> <Ty>
<Rzx> <Rzy> <Rzz> <Tz>
0 0 0 1
where
[ Position_in_ToCoordinateSystem_x ] = [ Rxx Rxy Rxz Tx ] * [Position_in_FromCoordinateSystem_x ]
[ Position_in_ToCoordinateSystem_y ] [ Ryx Ryy Ryz Ty ] [Position_in_FromCoordinateSystem_y ] [ Position_in_ToCoordinateSystem_z ] [ Rzx Rzy Rzz Tz ] [Position_in_FromCoordinateSystem_z ] [ 1 ] [ 0 0 0 1 ] [ 1 ]

## Slide 9: Commonly used
"Identity transform"
Does nothing
"Translation"
Pushes away
"Rotation"

## Slide 10: Careful with these!
"Scaling"
(and translation)
Anisotropic
scaling
(and translation)
"Skew"
(and translation)

## Slide 12: Rotation + translation
0 1 0 10
-1 0 0 0
0 0 1 0
0 0 0 1
1.
2.
The translation part always indicates the origin of the transformed coordinate system in the original coordinate system.

## Slide 13
I got a surface model (STL file) in centimeter units. But 3D Slicer assumes millimeters
What transform would convert it to millimeters?

## Slide 14
I got a surface model (STL file) in centimeter units. But 3D Slicer assumes millimeters
What transform would convert it to millimeters?
10 0 0 0
0 10 0 0
0 0 10 0
0 0 0 1
CmToMm

## Slide 15: Where do transforms come from?
Tracker device
Registration procedure
"Real-time"
Find
handedness
units
Get an idea about
origin
axes
Stay constant until next registration

## Slide 16: Registration
X
Y
Z
X
Y
Z
Reference
Tracker
Tracker-To-Reference-Transform
How do you find a constant transform?
Manual trials
Landmark (point) registration
Image registration
Landmark registration
Horn, 1987
Closed form solution
Min 3 points (+handedness)
a.k.a. "fiducial registration"

## Slide 17: What we call "calibration"
Registration between internal parts of objects
Constant relationship
X
Y
Z
X
Y
Z
Probe
Image
X
Y
Z
Stylus
X
Y
Z
StylusTip

## Slide 18: Programming transforms
# Create a transform node (unless already exists) that translates
referenceToRasTransform = vtk.vtkTransform()
referenceToRasTransform.Translate(30, 10, 0)
referenceToRas = slicer.util.getNode('ReferenceToRas')
if referenceToRas is None:
referenceToRas = slicer.vtkMRMLLinearTransformNode()
referenceToRas.SetName('ReferenceToRas')
slicer.mrmlScene.AddNode(referenceToRas)
referenceToRas.SetAndObserveTransformToParent(referenceToRasTransform)
Transforms can be stored in many variable types
vtkMatrix4x4 – SetElement and GetElement can get confusing
python list of lists – Confusing, no methods to operate
numpy.array – Great for numerical methods
vtkTransform – Great for understandable code
etc.

## Slide 19: Example: Image overlay
In-room Display
RAS
IJK
Overlay
Virtual Display
In-plane
calibration
Display reflection
calibration
Overlay frame
calibration
CT image
coordinates

## Slide 20: Coordinate systems in PLUS

## Slide 21: Example: Breast tumor tracking
Reference
Needle
Cautery
CauteryTip
Tumor
Needle
Probe
Image
Tumor
RAS

## Slide 22: Virtual endoscopy view

## Slide 23: Snap camera to centerline

## Slide 24: How would you change this?
Reference
Catheter
Camera
RAS

## Slide 25: Adding snap to camera transform
Catheter
Camera
Path
Reference
RAS

## Slide 26: Compute PathToCatheter
catheterToRas = vtk.vtkGeneralTransform()
catheterToReferenceNode.GetTransformToWorld(catheterToRas)
cathPosition_Cath = numpy.array([0.0, 0.0, 0.0])
cathPosition_Ras = catheterToRas.TransformFloatPoint(cathPosition_Cath)
pathPoint_Ras = numpy.array([0.0, 0.0, 0.0])
self.logic.closestPointFiducials(pathFids_Ras, cathPosition_Ras, pathPoint_Ras)
rasToCathether = vtk.vtkGeneralTransform()
catheterToReferenceNode.GetTransformToWorld(rasToCathether)
rasToCathether.Inverse()
pathPoint_Cath = rasToCathether.TransformFloatPoint(pathPoint_Ras)
pathToCatheterTransform = vtk.vtkTransform()
pathToCatheterTransform.Translate(
pathPoint_Cath[0], pathPoint_Cath[1], pathPoint_Cath[2])