## Slide 1: CAD and 3D printing
Tamas Ungi, Andras Lasso

## Slide 2: Whey learn CAD and 3D printing?
Make small tools (stylus, sim ultrasound, etc.)
Make sensor attachments
Make phantoms (anatomical, calibration)
Reproducible (share models, calibrate once)
Good printers under $250
Material cost ~$0.3 /g
Lots of fun!

## Slide 3
http://www.3dsystems.com/es/chefjet
http://n-e-r-v-o-u-s.com/blog/?p=4467
http://www.stratasys.com
1980s Presentation models, functional models…
… jewelry, clothes, toys, food...
http://media-2.web.britannica.com

## Slide 8: 3D printing process
Model preparation:
  Slice model into thin planes
  Add support structure
  Determine filling patterns
Print the model layer by layer
Finishing:
  Dissolve/remove support material
  Curing
  Sanding, filing
  Coating, polishing

## Slide 9: Slic3r - gcode generator

## Slide 10: Most common materials
tensile strength is measured by the maximum stress that a material can withstand while being stretched or pulled before breaking
glass transition is the reversible transition in amorphous materials from a hard "glassy" state into a viscous or rubbery state
 | ABS (acrylonitrile butadiene styrene) | PLA (polylactic acid)
Tensile strength | 27 MPa | 37 MPa
Elongation | 4 - 40% | 6%
Density | 1.0 - 1.4 g/cc | 1.3 g / cc
Melting point | 105 C - glass transition 230 C - extrusion | 60 C - glass transition 190 C - extrusion
Biodegradable | No | Yes (48 mo in water)
Examples | LEGO | Water cups, cutlery
Dissolve | Acetone | Methylene Chloride

## Slide 11: Why Autodesk vs. SolidWorks
Professional version is free with university email, $400 /yr otherwise vs. $4,000 + $1,200 /yr maintenance
Backwards compatible
Integrated sculpting and other mesh editor tools
Fewer files (components in a single file)
Enforced version control, online backup, teams
More robust modelling (non-manifold edges)
No need for complicated license management

## Slide 12: Autodesk Fusion 360
Download for free after registering an account with your university email address
Introductory tutorials can be completed in about 20 hours
Find lots of text/video help on Google for any specific problem

## Slide 13: Integrated data repository
Send your account email to ungi@queensu.ca to receive invitation to Perk Lab repository
With every save, you create a new version with a message
All versions are tracked with date, time, user, message
Export published versions using File / Export… menu in .f3d format

## Slide 14: Components and bodies

## Slide 15: Different workspaces
Drop down

## Slide 16: Capture or not – design history
Right-click component
select
check
Reduce design complexity during sculpting
Make multiple sketches available to each other for references

## Slide 17: Layer separation
Layers are strong but they are relatively easy to separate: important for thin and long parts
Which of these is going to break?

## Slide 18: Video: Toshiba clip design Live demo: - Sensor clip, reuse in other - Skull template