## Slide 1
Andras Lasso
3D Slicer Segmentation basics

## Slide 2: Segmentation
Head and neck RT phantom case
Also known as contouring
Delineates structures of interest
  Manual contouring: Slice by slice
  Automatic / semi-automatic
Omnipresent in medical imaging
  Surgical/radiation therapy planning
  Intra-operative navigation
  Volume/shape analysis
  3D printing (interventions)
  Education

## Slide 3: Representations
  Planar contours, Ribbons
    + Accurate 2D viewing and editing
    - Ambiguous in 3D
    - Poor 3D visualization
  Closed surface
    + Easy 3D visualization
    - Difficult to edit
    - May be invalid (e.g., self-intersecting), especially after non-linear transformation
  Binary labelmap
    + Easy 2D viewing and editing
    + Robust (always valid, even if transformed or edited)
    - Inaccurate (finite resolution)
    - Requires lots of memory if overlap allowed
  Fractional labelmap
    + Quite easy 2D viewing and editing
    + Robust
    + Quite Accurate
    - Requires lots of memory

## Slide 4: Data storage
Patient
Segmentation
Segmentation: MRML node, may contain multiple segments (each segment is a column)
Each segment contains multiple representations (each representation is a row)
Master representation:
  Editable
  All other representations are computed from this
  Stored persistently
Tumor (contour)
Segment: Tumor
Brain (contour)
Segment: Brain

## Slide 5: Conversion between representations
Driven by a dynamic graph
  Nodes are the representations
  Edges are the converters
    Can be dynamically added
    Can define representations
  Cost metrics for edges
Automatic conversion follows cheapest path
  Happens when an absent representation is requested
Contours
Ribbon
Binary image
Surface
Fractional image
1.5
2.5
3.5
2.5
2.0
4.0
2.0

## Slide 6: Slicer modules
Segmentations module:
  Create/delete segmentation nodes
  Create/delete/update representations
  Edit display properties
  Import from/export to different MRML nodes
  Copy/move segments
Segment editor module:
  Edit labelmap representation

## Slide 7: Hands-on
CTACardio
Thresholding
180-max
Apply
Disable surface smoothing, Show 3D
Crop to a kidney: Scissors, erase outside
Islands, Keep selected island, click on kidney
Undo 3x
Delete segment
Use for masking
Paint:
Segment vessel in right arm
Sphere paint
Erase
Draw

## Slide 8: Hands-on
Grow from seeds: contrast difference but not globally
MRBrainTumor1
Show 3D
Fix leakage
Apply
Smoothing
Segment stats
Grow from seeds: multiple segments
CTACardio
Paint, Sphere brush
4 segments, paint in 4 ventricles
Color smudge
Paint in an orthogonal view

## Slide 9: Hands-on
Masking:
Editable area: inside all segments
Paint
Grow
New segment, Outside all segments
Grow
New segment, Overwrite other segments (default)
Paint
Overwrite other segments: None
Fast marching:
Panoramix
Paint in a couple of blobs in the aorta and aneurysm
1% maximum
Subtract segment
Cut ends

## Slide 10: Hands-on
Hollow model:
Outside surface
Apply
Cut ends using Scissors effect
Fill between slices: geometric interpolation, tall segments
CTACardio
Abdominal muscles
Scissors:
CTChest, bone threshold
Island / Keep largest
Show 3D
Create new segment (for ribs)
Editable: inside all
Scissors - fill outside
Split islands to segments
Separate lowest vertebra with 3d scissors

## Slide 11: Hands-on
HD-BET:
Uses pytorch
MRBrainTumor1

## Slide 12: Hands-on
Slice thickness is used by paint tool 2D size
Segmentation on oblique slices
Segmentation on vesselness filtering result