## Slide 1: Volume reconstruction from AI-segmented ultrasound
Please cite these articles for methods presented:
Hu, Z., Nasute Fauerbach, P.V., Yeung, C. et al. Real-time automatic tumor segmentation for ultrasound-guided breast-conserving surgery navigation. Int J CARS (2022). doi: 10.1007/s11548-022-02658-4
T. Ungi et al., "Automatic Spine Ultrasound Segmentation for Scoliosis Visualization and Measurement," in IEEE Transactions on Biomedical Engineering, vol. 67, no. 11, pp. 3234-3241, Nov. 2020, doi: 10.1109/TBME.2020.2980540.

## Slide 2: Prerequisites – download data
Install 3D Slicer version 5.0.2 or later
Download tutorial data (.mrb scene and .h5 AI model )
  Data scene: Q006_SagittalSpineScan.mrb (size: 389 MB) https://1drv.ms/u/s!AhiABcbe1DByhMt5E3NjCmJ-RIlTZA?e=9Lqusg
  Trained AI model: SagittalSpine_05.h5 (size: 4 MB) https://1drv.ms/u/s!AhiABcbe1DByhMtwLY-z7kvKg1D5Ww?e=1loPhn

## Slide 3: Prerequisites – install extensions
Install extensions (plug-ins) for 3D Slicer
  SlicerOpenIGTLink: Communication interface to hardware
  SlicerIGT: Utility modules for IGT (registration and visualization)
  SlicerIGSIO: Infrastructure, algorithms module for IGT
  ParallelProcessing: Template for running Python scripts in parallel

## Slide 4
2. Search “igt” to find these modules
1. Open Extension Manager
3. Install

## Slide 5
1. Install ParallelProcesses extension too
2. Close, no need to restart Slicer yet

## Slide 6: Install TensorFlow in Slicer
Optional! If you want TensorFlow to use your GPU, install CUDA v. 11.3 and CuDNN v. 8.2
  For downloads and further instructions, check out the NVidia website: https://developer.nvidia.com/cuda-toolkit-archive
In Slicer / View/ Python Interactor use command:
>>> pip_install('tensorflow')
Once install process ends, you may test your environment:
>>> import tensorflow as tf
>>> tf.config.list_physical_devices()

## Slide 7
1. Open Python Interactor
2. Type commands here

## Slide 8: Clone the SlicerIGT/aigt repository
Clone aigt repository on your computer using: https://github.com/SlicerIGT/aigt
Locate SegmentationUNet.py file in your clone …aigt/SlicerExtension/LiveUltrasoundAi/SegmentationUNet/
Open Slicer / Edit / Application Settings / Modules
Drop the SegmentationUNet.py file in the area in Slicer settings called Additional module paths
Press OK on the Settings window and restart Slicer application

## Slide 9
1. Open Application Settings
2. Select Modules
3. Drag and drop .py file to this area from cloned source code
4. Restart Slicer!

## Slide 10: Data processing overview
Load Slicer scene with data
Set up input and output for segmentation module
Initialize prediction by updating input
Visualize prediction
Set up volume reconstruction
Start ultrasound replay
Set up volume rendering to visualize spine volume

## Slide 11
1. Click DATA
2. Click
3. Find tutorial data folder
4. Choose the .mrb file
5. Click
6. Click

## Slide 12
Switch to Segmentation UNet module

## Slide 13
1. Open file browser for AI model
2. Find .h5 model file in tutorial data folder
3. Click

## Slide 14
1. Select Image_Image as input volume
2. Create new volume for Prediction
1. Create new transform node for Prediction

## Slide 15
Make sure Sequence browser toolbar is visible

## Slide 16
1. Start the AI segmentation process
2. Step the recorded sequence so the AI process fully starts
On MacOS, uncheck this before Apply

## Slide 17
Switch to Four-Up layout

## Slide 18
3. Select Prediction to be shown in the green view
2. Make sure views are not linked
1.

## Slide 19
3. Drag and drop Prediction volume on PredictionToRas transform node
1. Switch to Data module
2. Select Transform hierarchy

## Slide 20
3. Show advanced option and flip the prediction image so it matches the ultrasound orientation
1. Switch to Volume Reslice Drive module (IGT category)
2. Select Prediction to drive green view

## Slide 21
3. Create a new volume and name it ReconstructedVolume for output
1. Switch to Volume Reconstruction module (IGT category)
2. Select these options
4. Press Start

## Slide 22
5. Press the play button to replay ultrasound scan (and reconstruct volume)

## Slide 23
1. Switch to Volume Rendering module
2. Select ReconstructedVolume
3. Select MR-Default preset
4. Visualize volume and see it in 3D view
5. Increase threshold to only show bones

## Slide 24
1. Switch to 3D-only view
2. Select Annotations
3. Hide R (ROI)
4. Stop playback when volume ready
(5. Stop Volume Reconstruction and Segmentation UNet modules too)