## Slide 1: Unlocking medical image files
Andras Lasso

## Slide 2: Motivation
How can I read this file that I received from a clinical collaborator?
What format should I choose to store my images?
How can I save this image in X format?
How can I modify this file (to anonymize, inject modified/processed data to other software)?

## Slide 3: Medical image file formats
Standard, commercially used
  DICOM
Standard, for research use
  MetaIO image
  NRRD
  NIfTI
  VTK
Proprietary
  Header + uncompressed raw data
  Other
Generic-purpose
  JPEG
  TIFF
  PNG ...
Don’t use!
No standardized medical metadata storage
Compression
Convert to a standard format as soon as possible
Don’t use! No image orientation. No metadata.
Very poorly designed. Only use for neuroimaging!
Similar to NRRD, but more limited. Not much reason to use it.

## Slide 4: Image metadata

## Slide 5: Basic image metadata
Dimensions: mostly 3 (3D spatial, 2D spatial + time), rarely 4 or more
Image size: typically a few-hundred pixels along each axis (512x512x512)
Pixel type:
  Scalar type: mostly 8-bit unsigned or 16-bit signed integer (can be also 32 or 64-bit, floating-point)
  Number of components: typically 1 (scalar), sometimes 3 (color or 3D vector)
Encoding: mostly non-compressed (raw), sometimes lossless compression (run-length encoding, deflate, ...), endianness

## Slide 6: Image pose
Origin, spacing, orientation: best defined by a linear transform, relative to a reference coordinate system
Reference
x
y
z
Image
x
y
z
Origin
Spacing and orientation

## Slide 7: Reference coordinate system
http://labmed.ascpjournals.org
http://www.vtk.org/Wiki/Proposals:Orientation
http://www.nature.com
Patient right is image left!
Patient right is image right!
There is no one single “correct” reference coordinate system.
Not a problem – as long as the coordinate system is properly specified.

## Slide 8: Reference coordinate system
Usually linked to patient anatomy (sometimes to the device)
  DICOM standard, ITK toolkit: LPS (reference coordinate system axis directions: patient’s left, posterior, superior)
  3D Slicer: RAS (right, anterior, superior)
  VTK toolkit: no arbitrary orientation is supported (only axis-aligned images)
Unit is millimeter
Origin is application-specific (usually center of the organ of interest)

## Slide 9: Medical image file formats
Standard, commercially used
  DICOM
Standard, for research use
  MetaIO image
  NRRD
  NIfTI
  VTK
Proprietary
  Header + uncompressed raw data
  Other
Generic-purpose
  JPEG
  TIFF
  PNG ...
  Single-file or header/pixel data are in separate files
  Various pixel types
  Optional lossless compression (deflate)
  Anatomical reference frame
  Extensible with custom fields
  Supported in ITK, VTK and 3D Slicer

## Slide 10: MetaIO
Originates from UNC, Chapel Hill, around 2000
Maintained by the Insight Software Consortium, Kitware
Extension: mha, mhd+zraw, mhd+raw
ObjectType = Image
NDims = 3
BinaryData = True
BinaryDataByteOrderMSB = False
CompressedData = True
CompressedDataSize = 102251258
TransformMatrix = -1 0 0 0 -1 0 0 0 1
Offset = 149.707 314.707 -949
CenterOfRotation = 0 0 0
AnatomicalOrientation = LPI
ElementSpacing = 0.585938 0.585938 2
DimSize = 512 512 472
ElementType = MET_SHORT
ElementDataFile = LOCAL
xœl½Y’cG¬e;ƒºR§'Òµ7ÿâã‰˜U–&)AžÆíÆüŠ3ŽØbýï¿ï¿q‹¿b‰ë¿?ÿþYcÿïßûçßÇç¿÷ÿ~ûþüößßß¿=>ß<?ÿ¿ÿ÷ï÷ïÏÿ½úþÖUÿ>?ŸÝ?¿Ùú»ÛŸ_>¿ÿÿúß÷Ïç…
http://www.itk.org/Wiki/ITK/MetaIO/Documentation

## Slide 11: MetaIO
Pro
  Can also store points, lines, tubes (for vessels, etc.), cubes, spheres, …
  Human-readable header
Con
  No standard way of specifying image dimensions
  ITK image reader implementation ignores patient orientation (https://issues.itk.org/jira/browse/ITK-1287 and http://www.na-mic.org/Bug/view.php?id=2173)
  Pushback against making changes or improvements (no funding, synchronized change in ITK and VTK, backward compatibility)

## Slide 12: NRRD (nearly raw raster data)
Univ. Utah, Chicago, BWH, from about 1998
Originally for diffusion-weighted imaging
Default image format for 3D Slicer
Extension: nrrd, nhdr
http://teem.sourceforge.net/nrrd/
NRRD0004
# Complete NRRD file format specification at:
# http://teem.sourceforge.net/nrrd/format.html
type: short
dimension: 3
space: left-posterior-superior
sizes: 343 362 144
space directions: (-0.58593749999999989,0,0) (0,-0.58593749999999989,0) (0,0,2)
kinds: domain domain domain
endian: little
encoding: gzip
space origin: (100.48828124999994,256.69921875,-641)
‹ T]|eÅõžàkÑçÛÝl’uÍîf“­³‹»k‹K±Bq/îî-…B±R ´@KbE…

## Slide 13: NRRD (nearly raw raster data)
Pro
  Strong support for generic N-dimensional images: each dimension can be described well with standard fields
  Human-readable header
Con
  Complete implementation is only available as part of a larger toolkit (teem). Trimmed-down versions are built into ITK and VTK are somewhat different.

## Slide 14: Sequence NRRD/Meta File format
Our Plus toolkit specifies custom fields for storing essential metadata for image-guided therapy (tracking data, ultrasound image sequences)
Custom extensions:
  ultrasound image orientation (image flip)
  per-frame image position and orientation
See complete specification here: http://perk-software.cs.queensu.ca/plus/doc/nightly/user/FileSequenceFile.html

## Slide 15: NIfTI
Developed and maintained by the Neuroimaging Informatics Technology Initiative (NIfTI) from about 2003
Developed for neuroimaging
Extensions: nia, nii, nii.gz
http://www.nitrc.org/projects/nifti/
\ r Wj €? ? ? @ °C €? úÈÂ€Y€Ã @ Ä ? € úÈÂ ? €€Y€Ã @ @ Ä n+1 üüüüüüüüüüüüüüüüüüü üüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüüü üüüü!üüüüüüüüüüüüüüüüüüüüüüüüüüü#ü,ü-ü'üüüüüüüüüüüüüüüüüüüüü.üWü¤üÖüÄüŸübü0üüüüüü'üBüSü‚üKýœþ‡ÿ»ÿeÿ]þýPü"üüüü'ü#ü#ü!üü%ü_üŽü¬üŽüaü[üÍüÅý þÔþUþlý•üAü%ü!ü#üü …

## Slide 16: NIfTI
Pro
  Used extensively neuroimaging (BIDS)
  Some multi-dimensional image support (but not generic)
  Clean, moderate-sized implementation (used by ITK)
Con
  Binary (not human-readable) header
  Lots of fields only useful for neuroimaging
  Storing custom metadata is practically impossible
  Ambiguities and redundancies in how image orientation is defined (sform and qform; what to do with non-orthogonal image axes, etc.)
  Many issues in its implementations

## Slide 17: Medical image file formats
Standard, commercially used
  DICOM
Standard, for research use
  MetaIO image
  NRRD
  NIfTI
  VTK
Proprietary
  Header + uncompressed raw data
  Other
Generic-purpose
  JPEG
  TIFF
  PNG ...
Supports various geometric objects
Good N-dimensional image support
Used a lot in neuroimaging

## Slide 18: Medical image file formats
Standard, commercially used
  DICOM
Standard, for research use
  MetaIO image
  NRRD
  NIfTI
  VTK
Proprietary
  Header + uncompressed raw data
  Other
Generic-purpose
  JPEG
  TIFF
  PNG ...

## Slide 19: Reverse engineering an unknown file
Web search based on extension and readable text in the file. Specification found? => Done
Open the file in a hex editor (e.g., PSPad)

## Slide 20: Reverse engineering an unknown file
Scroll into the middle of the data. Mostly slowly changing values?
No: Probably compressed data. Try web search, compare multiple files acquired with the same parameters, etc. to find out the compression method. Difficult.
Yes: Good. Probably simple uncompressed data.

## Slide 21: Reverse engineering an unknown file
Number of bytes per voxel: length of repeating byte pattern
1 byte per voxel (8 bit)
Repeating pattern of 2 bytes (00 and then around 15)
=> 2 bytes per voxel (16 bit)

## Slide 22: Reverse engineering an unknown file format
Install RawImageGuess extension in Slicer to guess:
Pixel type: usually 8 or 16 bit, trial and error for signed/unsigned
Endianness: trial and error
Header size: remove “random noise” from the beginning
Dimension: number of rows, columns, slices by trial and error
Spacing: usually just guessing (unless known from other sources, for example screenshots)

## Slide 23: X dimension (image width)
Repeating diagonal pattern => row length is too short/long
Width=512

## Slide 24: X dimension (image width)
Width=216
Width=256
Width=218
Width=220
Width=222
Width=224

## Slide 25: Y dimension (image height)
Frame 10
63 lines between them
=> Height = 220 – 63 = 157
Frame 11
Width=220
Height=220
Width=220
Height=220

## Slide 26: Header size
Frame 0
Frame 0
Width=220
Height=157
Width=220
Height=157
Offset to first image=26956
First pixel position: (116, 122)
=> Offset to first image = = 122*220+116 = 26956

## Slide 27: Reverse engineering an unknown file
NRRD0004
# Complete NRRD file format specification at:
# http://teem.sourceforge.net/nrrd/format.html
type: uchar
dimension: 3
space: left-posterior-superior
sizes: 271 148 180
space directions: (1.0, 0.0, 0.0) (0.0, 1.0, 0.0) (0.0, 0.0, 1.0)
kinds: domain domain domain
endian: big
encoding: raw
space origin: (0.0, 0.0, 0.0)
byte skip: 145622
data file: IMG_20181020_6_2.vol
Create NRRD image header (.nhdr)
Reverse-engineering the header:
Save images with different sizes and see how and where the header changes
Try to find the known image size etc. values in the header
Use the header file to load the volume into 3D Slicer
Don’t use a text editor to modify the header in a binary file, because text encoding and/or line end (CR/CRLF) conversion may modify the pixel data. Use a hex editor or choose a file format where the header and the pixel data are in separate files.
Notes: Example: c:\Users\andra\OneDrive\Projects\SlicerTesting2\20170831-GeDicomImport\data\20181020-FromSlicerForumPublic\IMG_20181020_6_2.vol

## Slide 28: Medical image file formats
Standard, commercially used
  DICOM
Standard, for research use
  MetaIO image
  NRRD
  NIfTI
  VTK
Proprietary
  Header + uncompressed raw data
  Other
Generic-purpose
  JPEG
  TIFF
  PNG ...